## Slide 1
Lecture 10
Dr. Mohammed Abdul Baset
Titrimetric Methods
Titrimetric analysis consists in determining the number of moles of reagent (titrant), required to react quantitatively with the substance being determined. The titrant can be added (a) volumetrically, with a glass or automatic burette or with a low flow-rate pump or (b) coulometrically, with an electrochemical generation from a proper electrolyte.
> Volumetric titrimetry
- The volume of a standard reagent is the measured quantity
> Gravimetric titrimetry
- The mass of the reagent is measured quantity
> Coulometric titrimetry
- The quantity of charge in coulombs required to complete a reaction with the analyte is the measured quantity
- The “reagent” is a constant direct electrical current of known magnitude that consumes analyte. The time required (and thus the total charge) to complete the electrochemical reaction is measured
- When the analytical reactions involve electron transfer. These methods are often called redox titrations.
Terms used in Volumetric Titrimetry
Titrant
Titrant is a substance added from the burette. Titrant used and reaction that proceeds usually defines name of the titration - like acid-base (or alkalimetric) titration if we use strong acid (or strong base) as a titrant, or redox when the reaction that proceeds is of a redox type. Name can be also much more specific - like permanganometric titration (also known as manganometry or permanganometry) when titrant is potassium permanganate.
Titration
A process in which a standard reagent is added to a solution of an analyte until the reaction between the analyte and the reagent is judge to be complete.
Back-titration
A process in which the excess of a standard solution used to react with an analyte is determined by titration with a second standard solution.
For example, the amount of phosphate in a sample can be determined by adding a measured excess of standard silver nitrate to a solution of the sample, which leads to the formation of insoluble silver phosphate:
The excess silver nitrate is then back-titrated with a standard solution of potassium thiocyanate:
52

## Slide 2
The amount of silver nitrate is chemically equivalent to the amount of phosphate ion plus the amount of thiocyanate used for the back-titration. The amount of phosphate is then the difference between the amount of silver nitrate and the amount of thiocyanate.
Equivalence Points and End Points
End point
The end point is express in range, the range should address to the equivalence point. End point is where the titration ends in practice. The closer the end point to the equivalence point the better, but it is often not easy to find a good method of equivalence point detection. However, very often, we can easily spot a point very close to the equivalence point - and that's where the end point will be.
The difference in volume or mass between the equivalence point and the end point is the titration error.
In volumetric methods, the titration error, Et, is given by
where Vep is the actual volume of reagent required to reach the end point and Veq is the theoretical volume necessary to reach the equivalence point.
Different methods to determine the endpoint include:
• pH indicator:
A pH indicator is a substance that it changes its colour in response to a chemical change. An acid-base indicator changes its colour depending on the pH (e.g., phenolphthalein). Redox indicators are also frequently used. A drop of indicator solution is added to the titration at the start; at the endpoint has been reached the colour changes.
• A potentiometer
It is an instrument that measures the electrode potential of the solution. These are used for titrations based on a redox reaction; the potential of the working electrode will suddenly change as the endpoint is reached.
• pH meter:
It is a potentiometer that uses an electrode whose potential depends on the amount of H+ ion present in the solution. (It is an example of an ion-selective electrode.) This allows the pH of the solution to be measured throughout the titration. At the endpoint, there will be a sudden change in the measured pH. This method is more accurate than the indicator method and is very easily automated. •
• Conductance:
The conductivity of a solution depends on the ions present in it. During many titrations, the conductivity changes significantly. (i.e., during an acid-base titration, the H+ and OH- ions react to form neutral H2O, this changes the conductivity of the solution.) The total conductance of the solution also depends on the other ions present in the solution, such as counter ions. This also depends on the mobility of each ion and on the total concentration of ions that is the ionic strength.
53

## Slide 3
• Colour change:
In some reactions, the solution changes colour without any added indicator. This is often seen in redox titrations, for instance, when the different oxidation states of the product and reactant produce different colours.
• Precipitation:
In this type of titration the strength of a solution is determined by its complete precipitation with a standard solution of another substance.
Equivalence point
Equivalence point is where the titration should really end - titration fraction equals exactly 1, we have added stoichiometric amount of titrant to titrated substance. That's not necessarily where we end titration.
Indicators
An indicator is a substance which is used to determine the end point in a titration. In acid-base titrations, organic substances (weak acids or weak bases) are generally used as indicators. They change their colour within a certain pH range.
Advantages of titration
There are several reasons why titration is used in laboratories worldwide:
1. Titration is an established analytical technique
2. It is fast
3. It is a very accurate and precise technique
4. A high degree of automation can be implemented
5. Titration offers a good price/performance ratio compared to more sophisticated techniques
6. It can be used by low-skilled and low-trained operators
7. No need for highly specialized chemical knowledge
Types of titrations
Titrations can be classified as:
1) Acid-base titrations or acidimetry and alkalimetry
2) Precipitation titrations
3) Complexometric titrations
4) Oxidation-reduction titrations or redox titrations 1
1) Acid-base titrations
When the strength of an acid is determined with the help of a standard solution of base, it is known as acidimetry. Similarly, when the strength of a base (alkali) is determined with the help
54

## Slide 4
of a standard solution of an acid, it is known as acid, it is known as alkalimetry. Both these titrations involve neutralisation of an alkali. In these titrations H+ ions of the acid combine with OH- ions of the alkali to from unionised molecules of water.
The end point in these titrations is determined by the use of organic dyes which are either weak acids or weak bases. These change their colours within a limited range of hydrogen ion concentrations, i.e., pH of the solution. Phenolphthalein is a suitable indicator in the titrations of strong alkalies against strong acids or weak acids, Methyl orange is used as an indicator in the titrations of strong acids against strong and weak alkalies.
The (acid-base) neutralization reactions are of the following four types:
1. A strong acid versus a strong base.
pH curve of strong acid (eg. HCl) and strong base (eg. NaOH) is vertical over the pH range 4-10. So the indicators phenolphthalein (pH range 8.3-10.5), methyl red (pH range 4.4-6.5) and methyl orange (pH range 3.2-4.5) are suitable indicators for such a titration.
2. A weak acid versus a strong base.
pH curve of weak acid (eg. CH3COOH) and strong base (eg. NaOH) is vertical over the pH range 7-11. So phenolphthalein is suitable indicator for such a titration.
3. A strong acid versus a weak base.
pH curve of strong acid (eg. HCl, H2SO4, HNO3) with a weak base (eg. NH4OH) is vertical over the pH range of 4-7. So methyl red and methyl orange are suitable indicators for such a titration.
4. A weak acid versus a weak base.
pH curve of weak acid and weal base indicators that there is no vertical part and hence, no suitable indicators can be used for such a titration.
55