## Slide 1: Lab(6) Glucose Test
Determination of Glucose Concentration in Serum by Glucose Kit
PRINCIPLE In the Trinder reaction1,2, the glucose is oxidized to D-gluconate by the glucose oxidase (GOD) with the formation of hydrogen peroxide. In the presence of peroxidase (POD), a mixture of phenol and 4-aminoantipyrine (4-AA) is oxidized by hydrogen peroxide, to form a red quinoneimine dye proportional to the concentration of glucose in the sample.

## Slide 2: REAGENT COMPOSITION
Monoreagent. Phosphate buffer 100 mmol/L pH 7.5, glucose oxidase > 10 KU/L, peroxidase > 2 KU/L, 4- aminoantipyrine 0.5 mmol/L, phenol 5 mmol/L.
Glucose standard. Glucose 100 mg/dL (5.55 mmol/L). Organic matrix based primary standard. Concentration value is traceable to Standard Reference Material 917b.